## Slide 1: Lecture 18 Input Capture with MC9S12C128
Real Time Control Issues
Automotive Applications
Real Time Interrupt
Input Capture with MC9S12C128
Input Capture Software Checklist
Input Capture to Measure Period on Channel 1
Pulse Accumulator on PT7 (Counter)

## Slide 2: Real Time Control with A Microcontroller
Direct interrupts
  IRQ, XIRQ, STRA
Able to generate output signals at specific time instants
  output compare
Able to capture external events when they occur
  measure the width of a pulse: input capture
  count the number of occurrences: pulse accumulator
Able to generate a periodic signal
  real time interrupt (RTI)
Able to generate pulse-width modulated signals
Able to understand analog signals: A/D converter

## Slide 6: Real-Time Interrupt RTI to Generate Periodic Interrupt
Enable bit RTIE in CRGINT Register
Flag bit RTIF in CRGFLG Register
RTR[6:4] prescale rate in RTICTL
RTR[3:0] modulus counter in RTICTL
A new RTI time-out period starts automatically
Writing to the RTICTRL will restart the period
In Clock and Reset Generation Module (CRGV4)

## Slide 7: Real-Time Interrupt RTI Clock Chain in RTICTL Register

## Slide 9: Eight Timer Channels: Output Compare & Input Capture
A channel can be either output compare or input capture. The same count registers TCi are used.

## Slide 11: Input Capture
To measure the width of a pulse
  Positive pulse, negative pulse or period
Store free running time TCNT into Timer Counter Registers on positive or negative or both edges
Smallest pulse width possible is one bus clock period
Largest pulse width is (216-1) x timer clock period

## Slide 12: The Resolution and Range of Input Capture
The smallest time interval for one count is the bus clock period.
The largest time interval for one count is the bus clock period times the largest prescaler value of 128.
The TNCT is 16 bits long and therefore the largest count is 216=65536
The largest time interval that can be measured is therefore
  (Bus Clock Period)*128*65535
  128*65535*1/2MHz=4.19 seconds

## Slide 13: Input Capture Selection
TIOS register
  IOSi=0 for Input Capture IOSi=1 for Output Compare
Precise measurement of a time internal
Capture events on pins PT7, ..., PT0 on PORT T, PTT
  events can be rising, falling or both edges in TCTL3 & TCTL4
Timer counts are stored in TC registers

## Slide 14: Input Capture Edge Action Options

## Slide 15: Flags and Count Storage
Input Capture Status Bits are Set When An Event Occurs
Input Capture Count Storage: two 8-bit registers TCiH and TCiL

## Slide 16: Input Capture Software Checklist
Initialize interrupt vectors if necessary
Set Bit-7 (TEN) in TSCR to enable timer
Reset bits in TIOS to enable input capture channels
Initialize EDGnB and EDGnA in TCTL3 and/or TCTL4 for triggering edges
Reset flags in TFLG1
Enable local interrupt bits in TMSK1
Enable global interrupt in code condition register
Poll flags to check actively or let interrupts occur
Get captured count value in TCn registers
Clear flags in TFLG1
* Page 323, Software and Hardware Engineering, F.M. Cady and J.M. Sibigtroth, Oxford University Press, 2000

## Slide 17: Input Capture Example on Channel 1 (IOC1) on PT1
Input edge
captured
TCNT
Timer interrupt flag register 1
Timer interrupt mask register 1
TMSK1
0 - no interrupt 1 - hardware interrupt request
TFLG1
0 - no 1 - input captured
16-bit timer count register
TC1
16-bit timer input capture/Output compare register 1
Timer system control register
TSCR
TEN
0 - disable timer 1 - enable timer
C1F
TIOS
Timer select register
0 - input capture 1 - output compare
IOS1
C1I
Timer control register 4
TCTL4
EDG1A
EDG1B
00 - disabled 01 - rising edges only
10 - falling edges only
11 - both edges

## Slide 18: Input Capture with Channel 1 on Port T Pin 1: Initialization
InputPin: EQU %00000010 ; pin 1 selected
EdgeA: EQU mTCTL4_EDG1A
EdgeB: EQU mTCTL4_EDG1B
CapturedValue: EQU TC1
DataSec: SECTION
First: DS 2
SignalPeriod: DS 2
CodeSec: SECTION
Initialize_Get_Period:
BSET TSCR1,mTSCR1_TEN ; Enable the timer system
BCLR TIOS,InputPin ; enable pin InputPin for input capture
RTS

## Slide 19: Input Capture with Channel 1 on Port T Pin 1: Get Period
Get_Period:
BSET TCTL4,EdgeA ; Initialize edge action for rising edge
BCLR TCTL4,EdgeB
BSET TFLG1,InputPin ; Clear Flag
; Wait for the first rising edge when IC1 Flag is set
spin1: BRCLR TFLG1,InputPin,spin1
; Now get the count that was latched
LDD CapturedValue
STD First ;Save it
BSET TFLG1,InputPin
; Wait for the second rising edge
spin2: BRCLR TFLG1,InputPin,spin2
LDD CapturedValue ; Get the ending count

## Slide 20: Input Capture with Channel 1 on Port T Pin 1: Get Period
CPD First
BHI SKIP ; no 2's complement if Second is greater than first
; Take 2's complement of First and add it to the second input capture.
COM First
COM First+1
LDX First ; 2's complement of the first count
INX
STX First
ADDD First
BRA RETURN
SKIP:
SUBD First ; Calculate the period
RETURN:
STD SignalPeriod
RTS
end

## Slide 21: Input Capture with Channel 1 on Port T Pin 1: main()
void SetOscillatorSpeed(void);
void SetLedindicator(void);
void Initialize_Get_Period(void);
void Get_Period(void);
extern unsigned int SignalPeriod;
void main (void)
{
uchar returned_value; unsigned int CalculatedPeriod;
Initialize_Get_Period();
while(1) {
Get_Period();
CalculatedPeriod = SignalPeriod*PRESCALER/PLLClock;
(void) printf("\n\r%s%i", "Signal Period in microseconds is ", CalculatedPeriod);
} //end while
}// end main

## Slide 22: Pulse Accumulator on PT7 (Counter)

## Slide 24: Pulse Accumulator Control Register PACTL
Two modes
  event-counting on PA7 (PAMOD=0) - pieces on an assembly line
  Gated time accumulation (PAMOD=1) - duration of a pulse
Edge detection
  PEDGE = 0 for falling edges and PEDGE=1 for rising edges

## Slide 25: Timer Clock Selection

## Slide 26: Pulse Accumulator Count Register (PACNT)